## Slide 1: Demo Day
Cameron, Sam, Lio, Ray, Diogo and Jose

## Slide 2: Design Requirements
Transversable area of 7” x 10”
Continuous 6N possible at the end effector
Moving speed up to 150 mm/s
Virtual wall stiffness of 1N/mm
Descoped for Alpha
Track two points of contact -> one point of contact
  One rotation of points, distance between points, etc.

## Slide 3: Mechanical - Alpha
Revised design
  Removed upside-down motor
  Updated link design to improve stiffness
  Refined stack on longer shaft
  Add limit switches
Waterjet and machined all custom components
Fully-assembled left-half linkage and 8020 frame
Mounted key components to 8020 Frame

## Slide 4: Mechanical - Beta
Improve backdrivability
  Analyze rotating components for ways to improve alignment & smoothness
Improve stiffness in the frame via gussets
Improve wire management
Add acrylic guards to remove pinch points

## Slide 5: Magnet
New selection of magnets to increase shear force (8 N), while sustaining normal force and low friction (4 N)
New puck design to allow for direct grounding
Notes: McMaster Magnet: 18N normal force
Polymagnet Magnet: 13.1N normal force
0.1N Shear force

## Slide 6: Electronics
Power Supply
Odrive
Motor
Gearbox
Encoder
Axis0
Motor
Gearbox
Encoder
Axis1
Touchscreen
STM32
Nvidia
HDMI
Driver
Touch
sensor
FFC
HDMI
Power
Power
FFC
USB
TX
TX
RX
RX
GND
GND
GND
TX
RX
Phase ABC
Phase ABC
3.3V GND A B Z
3.3V GND A B Z

## Slide 7: Electronics

## Slide 8: Embedded
Screen (u, v) pix Touch module
Screen (x, y) mm Resolution calculation
Top Magnet (x, y)mm – –
Button Magnet desired force (Fx, Fy) N Algorithm (e.g. stiff wall)
Button Magnet desired pos (x, y) mm Magnet (displacement - force) relationship
Arm EE(x, y)mm – –
Arm Angle(theta1, theta2) revolution IK solver

## Slide 9: Embedded
Basic Calibration
Using switch to get the absolute angle (incremental encoder)
Use Geometric relationship to calculate the screen arm transformation
Full Automatic Calibration – TBD
Let Motor be IDEL User move the Top Magnet
Read (u, v) and Arm angle (theta1 theta2)
Use multi Group data to solve all the unknown parameter.

## Slide 10: Demo!
Single-point tracking
Circular virtual wall