## Slide 1: Tablet Demo Day
Diogo, Lio, Ray, Jose, Sam and Cameron

## Slide 2: Introduction
What is a haptic device?
Machine that can simulate virtual objects with which a user may interact primarily via the sense of touch
Examples
  iPhone- keyboard clicks
  6DOF robotics arm with force-sensing hand and active glove
Our challenge:
Create an interactive 2D display (touchscreen) with active force feedback
  Up to 6N of force on the user

## Slide 3: How it works
Two, 2R parallel linkages
Magnets on the end effector go under the the screen and interact with magnets on top of the screen
Use tablet finger position data
2X brushless DC motor
2X 5:1 planetary gearbox
Common shaft / axis
2.5:1 XL timing belt reduction

## Slide 4: Demo 1: Sensing Functions
Translating the concept of a function into an haptic experience for visual impaired individuals

## Slide 5: Demo 2: virtual knob
Creating the physical experience of knob on a digital screen

## Slide 6: Demo 3: Knob + Shape sensing
Using a virtual knob to create the sensation of a shape